## Slide 1: I-TLC
Project: Design an intelligent traffic light controller and implement a Verilog code with a finite state model for its functionality.
Description :
This design aims to eliminate need of a traffic officer for control and clears the traffic in a better way.
For this,I have considered a four way road.one way is main road and other is side road.
Main road is considered to have huge traffic and has to be cleared as soon.
Side road is for the local people, both pedestrains and vehicles. Proper safety must be taken for crossing the road .These two roads are considered to be intersecting perpendicularly.
A sensor should also present at the side road which should sense high when a pedestrian or vehicles is observed on side road.

## Slide 2
This design prioritises to allow heavy traffic to flow .
Traffic rule that is followed-
Red light: The vehicle has to be stopped completely.
Yellow/Amber light: slow down your vehicle,move carefully and stop vehicle before Zebra lines.
Green light: You can move your vehicle at your speed.
Block diagram-
sensor
Clock Mainroad light
Reset Sideroad light

## Slide 3
State assignment and Declarations-
MSB denotes red light
LSB denotes green light
TL- Timer large( 10 sec)
TS- Timer small( 6 sec)
State Diagram-
State | Main road output | Side road output
S0 | 001 | 100
S1 | 010 | 100
S2 | 100 | 001
S3 | 100 | 010

## Slide 4
S0
S1
S2
S3
TL=1 + C=0
TL=0 & C=1
TS do not expire
TS expires
TL does not expire & C=1
TL expires & C=0
TS does not expire
TS expires

## Slide 5
Simulation result-